# Text boxes

Accessories:

1     1.Handle                    8.fuse

2. Aluminum frame            9. Anderson plug

3. Latches                   10. Battery clips

4. corner protection           11. Cable

5. Aluminum support legs      12. Handy carry bag

6.Junction box

7.Solar charger controller

100W（2X50W）12V

FOLDING SOLAR PANEL KIT

USER MANUAL

Trouble shooting if system does not function

A:Check all connections to ensure they are secure and free from moisture & debris

B:Protection of solar charger controller:

·PV Array Short Circuit

If PV array short circuit occurs, clear it to resume normal operation.

·Load Short Circuit

Fully protected against load wiring short-circuit. After one automatic load reconnect attempt, the fault must be cleared by reapply power or pressing the setting switch.

·Battery Reverse Polarity

Fully protection against battery reverse polarity, no damage to the controller will result. Correct the miswire to resume normal operation.

·Overheating Protection

If the temperature of the controller heat sink exceeds 85(C, the controller will automatically start the overheating protection.

·High Voltage Transients

PV is protected against high voltage transients. In lightning prone areas, additional external suppression is recommended.

Folding Solar Charging System Specification

| Type | Module Size | N.W | Specification |
| --- | --- | --- | --- |
|  |  |  | Max-Power | Max-Power Voltage | Max-power Current | Open-Circuit Voltage | Short-circuit Current |
| Module | mm | Kg | W | V | A | V | A |
| 2*50w | 505*690*60 | 10 | 100 | 17.5 | 5.71 | 21.6 | 6.17 |

Disclaimer of Liability and Warranty

warrants the solar panel of the Portable Solar Kit for 25 years, 1 year for the cable and componets and 3 years for the controller. This warranty is vaild against defects in materials and workmanship. It is not valid against defects resulting from, but not limited to:

• Misuse and/or abuse, neglect, or accident

• Exceeding the unit’s design limits

• Improper installation, including, but not limited to, improper environmental protection and improper hook-up

• Acts of God, including lightning, floods, earthquakes, fire, and high winds

• Damage in handling, including damage encountered during shipment or installation.

Installation

- Locate in a clear sunlit area free from over hanging branches or obstructions.

- Remove solar panel kit from handy carry bag.

- Unclip the two latches on the side of the unit and fold two panels outward. Extend the two stands to their maximum length and lock in position.

- Place solar panel kit in the position facing the sun.

Note: To obtain maximum output it is suggested that the panels’ direction be frequently adjusted to track the suns movement through the day.

- Fully extend battery lead and connect to waterproof solar charger controller and ensure that battery clips do not come in contact with one another. Connect battery clips to the + positive (red) &-negative (black) battery terminals. Ensure that the connection is secure.

FEATURES

Modular and Durable Integrated Design with High Efficiency Monocrystalline Solar Modules

Panels are built with strong anodized aluminum frames and high transparency solar

glass for maximum light permeability and high efficiency.

Solar charger controller

Configure the most advanced LCD solar controller. The operation mode of the controller, Please refer to separate Owners Manual for the Charge Controller for details.

FREQUENTLY ASKED QUESTIONS

Q. What type of batteries can be used with the kit.

A:.1. Sealed lead acid battery   2. Gel battery   3. Flooded battery

Q. Will the solar panels over charge my battery.

A. The charge regulator ensures that a steady charge is supplied to the battery and will not be over charged.

Q. Can I extend /lengthen the battery lead.

A. If the lead is extended this can result in a loss of voltage and insufficient power transferred from the solar panels to charge the battery

Q. How do I clean the solar panel.

A. Dust & dirt should firstly be swept off the panel surface using a soft brush and then use a wet cloth to wipe the panel surface to remove remaining dirt & grime. It is recommended that any bird droppings be removed as soon as possible as if left can cause damage to the surface.

12